# Symbol LS3578 CareFusion IMPRESS Setup

Prerequisites and Notes:

- All page references are from the LS3578 Product Reference Guide.

- Scanner should be fully charged as specified on page 1-8.

- Connect the Cradle to the PC

USB connection to a host. The scanner autodetects a USB host and defaults to the HID keyboard interface type. Select other USB interface types by scanning programming bar codes.

Important: Connect the interface cable and power supply (if necessary) in the following order to ensure proper operation of the scanner and cradle.

- Insert the interface cable into the cradle's host port.  If necessary, connect the power supply to the cradle's power port (if the interface requires, or to allow fast charging of the scanner).  If applicable, thread the interface cable over the cable support hook and run the host and power cables into their respective cable grooves.

NOTE: On first installation when using Windows, the software displays a prompt to select or install the Human Interface Device driver. To install the Human Interface Device driver provided by Windows, click Next through all the choices and click Finished on the last choice. The scanner powers up during this installation.

- Connect the other end of the interface cable to the host.

- Pair the scanner to cradle

Pairing registers a scanner to the cradle such that the scanner and cradle can exchange information. Pair the scanner to the cradle either by inserting it in the cradle (if pairing on insertion is enabled), or by scanning the pairing bar code. The cradle includes pairing bar codes on both its front and back. To pair the scanner with the cradle, scan a pairing bar code. A high-low-high-low beep sequence followed by a low-high beep sequence indicates successful pairing and connection to the remote device. A long low, long high beep sequence indicates unsuccessful pairing.

- Add a Carriage Return/Enter

To program a carriage return/enter after each bar code scanned, scan the following bar codes in order:

- Enable Code 39 full ASCII

Troubleshooting

See table 3-1 starting on page 3-2.

Reset the scanner to factory defaults

After scanning the factory default barcode re-pair the scanner with the cradle.

For factory default values, see Table A-1 on page A-1.

Basic Scanner Information

The Symbol LS3578 scanner combines excellent scanning performance and advanced ergonomics to provide the best value in a lightweight laser scanner, ensuring comfort and ease of use for extended periods of time.

Inserting the Battery: The battery resides in a chamber in the scanner handle. To insert the battery:

- Insert a coin or flathead screwdriver in the slot at the base of the scanner, then turn the slot counterclockwise to release the latch.

- Lift the latch.

- If a battery is already installed, turn the scanner upright to slide the battery out.

- Slide the new battery into the chamber, with the rounded side toward the back and the contacts facing into the chamber.

- Close the latch.

- Insert a coin or flathead screwdriver in the slot at the base of the scanner, press down gently, and turn the slot clockwise to lock the latch in place.

Beeper and LED Definitions:

See tables starting on page 2-1

Beeper Volume:

Scan the applicable barcode to set the beeper volume: